# F6CTE (Patrick Lindecker) the 25th of December 2008

# THE CALL ID EASY WITH MULTIPSK (4.12)

## Introduction and main use

This document explains how to use the Call ID.

This "Call ID" ("Call" for "Call sign") identifier can be, automatically, detected and located. It can be any Call sign or Call sign 6 characters + Locator. The Call ID is always detected at -13 dB (first decodings at -18 dB), so with a sensitivity better than the PSK31 one. The central frequency of the identifier (which is also the central frequency of the transmission), is determined with a precision of +/- 2.7 Hz. As soon as this identifier (without any error) is received, Multipsk:

* display the call sign (possibly preceded by "CQ ") and the Locator on the waterfall,

* display, on the waterfall,  the call sign, possibly preceded by "CQ " and possibly followed by "Emergency!" (and a short ring) and  
      the Locator,

* display the time of reception, the call sign, the Locator and the Signal to Noise ratio in the Call ID reception window,

* switch on the received frequency (optional),

* display the position the Locator on a map (optional).

This identifier is transmitted in 3.3 sec and has a bandwidth of 172 Hz.  It is composed of a RS ID (code 153) followed by a sequence of 56 bits of data and 24 bits of CRC.

Notes about the help in Multipsk:

- To bring up the text help (contextual one), click on the right button of the mouse, with the focus over the mode button "ALE400", for example).

- Also use the button hints (wait a fraction of second over a button).

Further are several snapshots which explain how to use the Call ID (main functions).

Refer to the help for more advanced options (beacon, CALL_ID.TXT storage file...).

Preparation of the Call ID

Buttons to push to start automatic decoding or to transmit a Call ID

Reception of a Call ID (call sign + Locator) on the RX/TX screen

Log book of the Call Ids